## Slide 1: Kinect

## Slide 2: Prototype Presentations

## Slide 3: Kinect Sensors
3D Depth Sensors: light and right
RGB Camera: center

## Slide 4: Kinect
Kinect uses structured light
Body position is inferred using machine learning
Depth map is constructed by analyzing a speckle pattern of infrared laser light

## Slide 5: What is structured light?

## Slide 6: Project a known pattern onto the scene and infer depth from the deformation of that pattern

## Slide 7: Kinect Resources
Open NI
http://developkinect.com/resources
TSPS – Toolkit for Sensing People in Spaces

## Slide 8: Getting Started

## Slide 9: Up & Running
ofApp.h
#include “ofxKinect.h”
ofxKinect kinect;
ofApp.Cpp
Setup
kinect.setRegistration(true)
kinect.init()
kinect.open();
Update
kinect.update()
kinect.draw(0, 20, 400, 400);
kinect.drawDepth(0, 280, 400, 400);
Notes: kinect.setRegistration(true) – enables depth/video image calibiraiton

## Slide 10: Controlling the Angle
ofApp.h
int angle;
ofApp.Cpp
Setup
angle = 15;
kinect.setCameraAngle(angle);
Keypressed
switch (key) {
case OF_KEY_UP:
angle++;
if(angle>30) angle=30;
kinect.setCameraTiltAngle(angle);
break;
Case OF_KEY_Down:
}

## Slide 11: Adding a Mesh

## Slide 12: Adding a Mesh
ofApp.h
#include "ofxOpenCv.h”
void drawPointCloud();
ofxCvGrayscaleImage depthImage;
ofEasyCam easyCam;
ofApp.Cpp
Setup
depthImage.allocate(kinect.width, kinect.height);
kinectAnglePitch = 0;
kinect.setCameraTiltAngle(kinectAnglePitch);
cameraZoom = -1000;
Update
if(kinect.isFrameNew()) { depthImage.setFromPixels(
kinect.getDepthPixels(),
kinect.width, kinect.height);
depthImage.flagImageChanged();
}

## Slide 13: Adding a Mesh
ofApp.Cpp
void testApp::drawPointCloud(){
int w = kinect.width;
int h = kinect.height;
ofMesh mesh;
mesh.setMode(OF_PRIMITIVE_POINTS);
int step = 1;
for (int y = 0; y < h; y += step) {
for (int x = 0; x < w; x += step) {
if (kinect.getDistanceAt(x, y) > 0) {
mesh.addColor(kinect.getColorAt(x,y));
mesh.addVertex(kinect.getWorldCoordinateAt(x, y));
}
}
}
glPointSize(2);
ofPushMatrix();
ofScale(1, -1, -1);
ofTranslate(0,0, cameraZoom);
ofEnableDepthTest();
mesh.drawVertices();
ofDisableDepthTest();
ofPopMatrix();
}
ofApp.Cpp
Draw
easyCam.begin();
drawPointCloud();
easyCam.end();

## Slide 14: blobs

## Slide 15: Movement tracking in OpenCV is done with blobs

## Slide 16: blobs
Data object that represents a contiguous area of a frame
Contrast caused by the difference between adjoining pixels

## Slide 17: Tracking
Tracking is the process of identifying one or more objects that display consistent movement within the field of the computer’s vision and identifying those objects over time

## Slide 18: ofxCvCounterFinder
Class that performs the blob finding and tracking task
findCountours()
    virtual int findContours( ofxCvGrayscaleImage& input,
    int minArea, int maxArea,
    int nConsidered, bool bFindHoles,
    bool bUseApproximation = true);

## Slide 19: findCountours()
Input: this is an ofxCvGrayscaleImage that searched for bobs
minArea: this is the smallest potential blob size that will be considered as a blob for the app
maxArea: this is the largest potential blob size
nConsidered: max number of blobs to consider
bFindHoles: tells the contour finder to try to determine whether there are holes within blob detected
bUseApproximation: tells if to use approximation and to set the minimum number of points needed to represent a certain blob (example line)
Notes: So if I’m detecting fingers, what is nconsidered? How about hands?

## Slide 20: ofxCvCounterFinder Properties
Blobs: this is a vector ofxCvBlob which returns each blob that was found in the image
nBlobs: int that returns the number of blobs
For (int I = 0; I < countourFinder.nBlobs; i++){
countourFinder.blobs[i].draw(200, 200);
}

## Slide 21: ofxCvBlob class
Area: size of blob in pixels
boundingRect: ofRectangle that shows height and width of your blob
Centroid: ofPoint instance with its x and y positions for the center of blob
Hole: boolean whether blob contains a hole
Pts: vector of ofPoint objects; this list the different points around the edge of the blob
nPts: int representing the number of points in the contour
Void draw(float x, float y): draws the blob with x,y as the upper left hand corner

## Slide 22: Blob Detection
ofApp.h
ofxCvColorImage colorImg;
ofxCvGrayscaleImage grayImage;
ofxCvGrayscaleImage grayThreshNear
ofxCvGrayscaleImage grayThreshFar;
ofxCvContourFinder contourFinder;
bool bThreshWithOpenCV;
int nearThreshold;
int farThreshold;
vector<ofPoint> cursors ;
ofxPanel gui;
ofxIntSlider threshHoldNear;
ofxIntSlider threshHoldFar;
These images are used to determine what has changed between the current frame and the background. grayImage converts the colorImage into a grayscale
Each frame we take a number of blobs and create cursors at their centroids

## Slide 23: Blob Detection
ofApp.cpp
Setup
gui.setup();
gui.add(threshHoldNear.setup("Near Threshhold", 100, 0, 255));
gui.add(threshHoldFar.setup("Far Threshhold", 95, 0, 255));
colorImg.allocate(kinect.width, kinect.height);
grayImage.allocate(kinect.width, kinect.height);
grayThreshNear.allocate(kinect.width, kinect.height);
grayThreshFar.allocate(kinect.width, kinect.height);
bThreshWithOpenCV = true;
Set GUI Up
Allocate memory for the array of pixels that the image will use to save the incoming pixel data.

## Slide 24: Blob Detection
ofApp.cpp
UPdate
nearThreshold = threshHoldNear;
farThreshold = threshHoldFar;
kinect.update();
if(kinect.isFrameNew()) {
grayImage.setFromPixels(kinect.getDepthPixels(), kinect.width, kinect.height);
if(bThreshWithOpenCV) {
grayThreshNear = grayImage;
grayThreshFar = grayImage;
grayThreshNear.threshold(nearThreshold, true);
grayThreshFar.threshold(farThreshold);
cvAnd(grayThreshNear.getCvImage(), grayThreshFar.getCvImage(), grayImage.getCvImage(), NULL);
}
}
grayImage.flagImageChanged();
contourFinder.findContours(grayImage, 10.0 , (kinect.width * kinect.height) / 4 , 2, false );
cursors.clear() ;
Transfer Gui Values
If we are connected and there is a new frame rate, we load grascale image and assign thresholds.
Find contours and clear our cursors vector.

## Slide 25: Blob Detection
ofApp.cpp
Update
cursors.clear() ;
for ( int i = 0 ; i < contourFinder.nBlobs ; i++ ){
ofVec2f iCentroid = contourFinder.blobs[i].centroid;
cursors.push_back( iCentroid ) ;}
Draw
grayImage.draw(0, 0, kinect.width , kinect.height);
contourFinder.draw(0, 0, kinect.width, kinect.height);
gui.draw();
if ( cursors.size() > 0 ) {
for ( int i = 0 ; i < cursors.size() ; i++ {
ofSetColor(255, 0, 0);
ofCircle( cursors[i] , 12 ) ;
}
}
Find contours, add centroids, and draw them.

## Slide 26: Final
Working Demo of
Series of prototypes in the form of sketches that eventually lead you to your final
Technical presentation on sketch